### Praesideo Call Station Interface PRS-CSI

### Architects’ and Engineers’ Specifications

The call station interface shall have a network interface for fiber optical hybrid cabling with dual network connections, capable of redundant loop operation. The fiber optic network interface shall support multi-channel digital audio and control signals.

The call station interface shall act as an interface to a remote call station that does not have direct network connectivity. Via the call station interface, the remote call station shall be able to receive audio and operational control signals from the network and report its status to the system controller.

It shall use CAT-5 UTP cable for interconnection with a length of up to 1000 m. The CAT-5 cable shall carry the audio and control signals in digital format.

It shall contain a digital audio processor for the remote call station with a 3-band fully parametric equalizer and semi parametric shelving equalizers for bass and treble control.

The call station interface shall be remotely configurable via the network interface and it shall be powered from the network for easy installation or from an external (backup) power supply.

It shall provide two supervised control inputs to pass power supply status information, from e.g. a UPS, to the controller of the system, via the network.

It shall have a supervision system to monitor its functions and operation in compliancy to the standards EN 60849 and EN 54-16. Fault conditions of the unit itself and the connected remote call station shall be reported by the unit to a network connected system controller for logging purposes.

The unit shall be able to operate at a maximum operating temperature of 55°C.

The call station interface shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The call station interface shall be a Praesideo PRS-CSI, manufactured by Bosch Security Systems.