### Praesideo Call Station Keypad LBB4432/00

### Architects’ and Engineers’ Specifications

The call station keypad shall have a serial digital interface to connect it to a basic call station or call station kit with loop through facilities for additional keypads.

The call station keypad shall provide 8 keys and 8 bicolor green/yellow LEDs, that can be configured via the network to provide various functions for the call station, it is connected to.

The configuration shall allow for selection functions and control functions to be programmed for each key.

It shall be possible to configure the keys for different modes of operation, such as momentary or toggle operation. Each key shall have one bicolor status LED beside it.

Beside each key a transparent, removable tab shall be available that can hold a label for the key. Safety covers to prevent accidental activation of the keys shall be available as an option.

The keypad shall get its power from the call station it is connected to.

The unit shall be able to operate at a maximum operating temperature of 45°C.

The call station keypad shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The call station keypad shall be a Praesideo LBB4432/00, manufactured by Bosch Security Systems.