### Praesideo Call Station Keypad Kit LBB4434/00

### Architects’ and Engineers’ Specifications

The call station keypad kit shall be a printed circuit board, providing connections for switches and indicators to enable an installer to create custom build call station panels in combination with a call station kit. It shall have a serial digital interface to connect it to a basic call station or call station kit with loop through facilities for additional keypads or keypad kits.

The keypad shall provide connections for 8 switches (keys) and 16 LEDs, that can be configured via the network to provide various functions for the call station, it is connected to.

The configuration shall allow for selection functions and control functions to be programmed for each switch.

It shall be possible to configure the switches for different modes of operation, such as momentary or toggle operation. Each switch shall have 2 complementary LEDs for status indication.

The keypad based on the kit shall get its power from the call station it is connected to.

The unit shall be able to operate at a maximum operating temperature of 55°C.

The call station keypad kit shall be certified by an independent test agency, such as the German TÜV, for compliancy to the standards EN 60849 and EN 54-16 for emergency sound systems.

The call station keypad kit shall be a Praesideo LBB4434/00, manufactured by Bosch Security Systems.